## Slide 1
COLOR DETECTOR – HARDWARE CONNECTION
Breadboard
+
-
UNO R3 with USB
Color Sensor TCS 3200
16x2 LCD screen with I2C
SCL
SDA
VCC
GND
A4
A5
5V
GND
2
~3
4
~5
~6
GND
LED
OE
G
V
OUT
S3
S2
S1
S0
USB

## Slide 2
COLOR DETECTOR – HARDWARE OVERVIEW
Breadboard
+
-
UNO R3 with USB
Color Sensor TCS 3200
(input)
16x2 LCD screen with I2C
(output)
SCL
SDA
VCC
GND
A4
A5
5V
GND
2
~3
4
~5
~6
GND
LED
OE
G
V
OUT
S3
S2
S1
S0
USB
POWER
Flash
SERIAL

## Slide 3
I2C
16x2 LCD screen with I2C
16x2 LCD
D0
D1
D2
D3
D4
D5
D6
D7
1
0
1
1
0
1
0
0
-
LiquidCrystal_I2C lcd(0x27, 16, 2);
void setup()
{
lcd.begin();
lcd.clear();
lcd.setCursor(0,0);
lcd.write(‘-’);
}
SDA: Serial Data Line
SCL: Serial Clock Line
Interface I2C 16x2 LCD with Arduino Uno (Just 4 wires) - Arduino Project Hub
sketch.ino - Wokwi Arduino and ESP32 Simulator

## Slide 4
#define s0 6
#define s1 5
#define s2 4
#define s3 3
#define out 2
Color Sensor TCS 3200
UNO R3
2
4
3
~6
~5
// Set highest output frequency scalling
digitalWrite(s0,HIGH);
digitalWrite(s1,HIGH);
void loop()
{
digitalWrite(s2,LOW);
digitalWrite(s3,LOW);
red = GetData();
digitalWrite(s2,LOW);
digitalWrite(s3,HIGH);
blue = GetData();
digitalWrite(s2,HIGH);
digitalWrite(s3,HIGH);
green = GetData();
delay(2000);
}
unsigned long GetData(){
data=pulseIn(out,LOW);
delay(20);
return data;
}
1
2
3
Color Detection Using TCS3200/230 - Arduino Project Hub

## Slide 5
UNO R3 with USB
Flash
Serial (debug information only for programmer)
Arduino serial monitor
SERIAL
void setup() {
// put your setup code here, to run once:
Serial.begin(9600);
Serial.print("\nHello, Mo!\tThis is your new world!\n");
}
void loop() {
// put your main code here, to run repeatedly:
Serial.print(“still running, no bug! :-)\n”);
delay(1000);
}
Hello, Mo! This is your new world!
Still running, no bug! :-)
Still running, no bug! :-)
Still running, no bug! :-)

## Slide 6
Serial (configuration)

## Slide 7
About Colors
lcd.clear();
if (red < blue && red < green){
Serial.println("\tRed Color");
lcd.print("Red Color");
} else if (blue < red && blue < green){
Serial.println("\tBlue Color");
lcd.print("Blue Color");
} else if (green < red && green < blue){
Serial.println("\tGreen Color");
lcd.print("Green Color");
} else if (red == green && red == blue){
Serial.println("\tGreyscale");
lcd.print("Greyscale");
} else if (red == green){
Serial.println("\tYellow color");
lcd.print("Yellow color");
} else {
lcd.print("invalid color!");
}